## Slide 1
Project Supervisor : Prof.Dr. Benedikt Dietrich
Master project of the student : Siamak Mirifar
RoboSoccer – Design and development of an image processing system
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Notes: grüß ihnen, Herzlich willkommen alle zu meinem heutigen Präsentation
Mein heutiger Präsentation wird sich mit der Bildverarbeitung von SSL RoboSoccer befassen.
Weil das gesamte Projekt noch nicht fertig ist, werde ich nur meinen Teil unterstützen, und wir werden zusammen durch den gesamten Prozess führen

## Slide 2
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Brief Description
1: Goal My Project
2: The Construction
Notes: My project is limited to a vision system that sends the position of the ball and each robot to each team's software, and with this information, each team running on the server can remotely control the robots on the soccer field.
The setup consists of the robots, a vision system, and a server. The image processing system detects both the robots and the position of the ball on the soccer field.

## Slide 3
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Challenges of the project
Video recording
Image processing
Robot pattern recognition
Real-time data processing and application performance
Server connection
Graphical user interface (GUI)
Notes: 2- The video resolution should be high enough to detect robots and low enough to allow fast image processing.
3- What image processing methods should be used?
4- How to give ID to robots?
5- How can we speed up the process?
6- ....
7- GUI to connect all the functions together (In my presentation I use the term GUI.

## Slide 4
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Structure of the soccer field
Camera: Logitech Brio 4k
Field size : 277*188 cm
Background color : Dark green
Material: Carpet
Robot radius size : 85 cm
Structure :
Notes: The sensor is a Logitech Ultra HD (4K). The sensor supports multiple resolutions, including 4K at 30 fps, 1080p at 30 or 60 fps, and 720p (HD) at 30, 60, or 90 fps.
It is important to note that the fps depends on the length of the cable and the quality of the cable. For example, if we use USB 2, we will have lower fps or if we use a very long cable with low quality, the fps will be reduced.
Also it is important to have a dark green background, then it is easier to recognize robots later.

## Slide 5
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Image Processing
OpenCV
Loading image
Video recording
http://opencv.willowgarage.com/wiki/OpenCVLogo
Possibilities of image processing :
Notes: I have used OpenCv for capturing videos and images.... OpenCV (short for Open Computer Vision) is a free program library of algorithms for image processing and computer vision. OpenCV is written for the programming languages C, C++, Python and Java and is available as free software.
The advantage of OpenCV is that it gives us the ability to upload images and capture video at very high FPS.
It also helps us with image processing to find robots and their position.

## Slide 6
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Image Processing
Reduce the image size
Blue color detection
Is the area of the blue circle is accepted ?
Saving the pixel position
Steps through the process :
Notes: 1- To speed up the process, we reduce the image resolution from 4k to 1080p.
2- The first and most important step in finding the robot is to look for the blue circle on the field.
3- After finding the blue circle, we check if its size is sufficient. If so, I save the pixel position of the circle.

## Slide 7
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Image Processing
The captured images are in RGB color space.
To detect the blue color, we need to use the HSV color space.
https://en.wikipedia.org/wiki/HSL_and_HSV
https://de.wikipedia.org/wiki/RGB-Farbraum
Color space:
Notes: An RGB color space is an additive color space that replicates color perceptions by additively mixing three primary colors (red, green, and blue). Human color vision is characterized by three cone types.
The HSV color space is the color space of several color models. Here the chromaticity coordinate of a color is defined with the help of the three coordinates:
Color value (English hue): Color angle on the color wheel (0° for red, 120° for green, 240° for blue)
Color saturation: (0% = neutral gray, 50% = little saturated color, 100% = saturated, pure color)
Brightness value (value; also called darkness level): (0% = no brightness, 100% = full brightness)

## Slide 8
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Image Processing
Mask :
In OpenCV, by specifying the lower limits of the color and the upper limits of the color (blue in our case), we can disable all other color spaces.
Notes: Was bedeutet Maske?
In opencv by specifying the lower limits of color and upper limits of color (in our case blue color) we can disable(delete) all other color range.

## Slide 9
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Image Processing
Mask :
Notes: Here we have another view of the same image, which also shows the main image, and we can see the result of masking

## Slide 10
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Image Processing
Contours :
Areas that are not included
Contours can be simply explained as a curve that connects all points constantly (in sequence) that have the same color or intensity (in our case, the color mask is blue).
Notes: Contours can be simply explained as a curve that connects all constantly (follow in series) points that have the same color or intensity (in our case the color mask is blue) . The contours are a useful tool for the detection of objects.
!!! As you can see in the picture, the contours can also contain image noise that causes unwanted area.
To avoid this unwanted area, I calculated the needed area (based on pixels) and saved the contours that are in the desired Bereic/area.

## Slide 11
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Image Processing
Crop image :
Notes: After finding the pixel position of the blue circle, I can crop the image based on the pixel position.
and now we have our robot in the image.

## Slide 12
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Recognition of robot patterns
1
2
3
4
5
6
7
8
9
10
11
12
13
14
15
16
Pattern :
Notes: Im nächsten Schritt möchte ich den Winkel und die Roboter-ID des Roboters herausfinden.
wie wir sehen können, gibt es 16 Roboter, mit verschiedenen Farbmustern.
Was soll ich tun?
Kreis

## Slide 13
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Recognition of robot patterns
1
2
3
4
https://github.com/RoboCup-SSL/ssl-vision/blob/master/patterns/teams/standard/standard2010_template_all_dimensions.pdf
Pattern recognition :
Notes: As you can see, we have pattern which us available from SSLROBOCUP Github that shows how a robot should be seen from above.
to find an ID, first I have to find the angle
1- First I divided the picture into 4 parts

## Slide 14
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Recognition of robot patterns
1
2
3
4
Negative-Angle
Positive-Angle
DOWN_LEFT
TOP_LEFT
DOWN_RIGHT
TOP_RIGHTS
0˚
180˚
Notes: To calculate the angle, I had to define a reference. Therefore, I consider the right side of the image as a positive angle, and the left side as a negative angle. In this case, the robot is almost -40 from the reference.

## Slide 15
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Recognition of robot patterns
1
2
3
4
Negative-Angle
Positive-Angle
DOWN_RIGHT
TOP_LEFT
DOWN_RIGHT
TOP_RIGHT
Notes: To find the angle, I first find the shortest line between the centers of all the circles.
In this case both circles are at position 4, bottom right.
then I draw an (imaginary/imagined ) line from the pixel with the smallest x-position value

## Slide 16
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Recognition of robot patterns
1
2
3
4
Negative-Angle
Positive-Angle
DOWN_LEFT
TOP_LEFT
DOWN_RIGHT
TOP_RIGHT
Notes: Since it is clear, I could calculate the angle with the tangent function

## Slide 17
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Recognition of robot patterns
finding robot:
Notes: Then I rotated the image by the found degree
In the last step I used contours and masks to find the red and green circles and their pixel positions. And by matching with the predefined list I could find out the robot ID.

## Slide 18
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Recognition of robot patterns
The final results for all robots with the same pattern recognition:
Notes: As you can see, all other robots are detected using the same method and the angles of the robots are quite accurate.

## Slide 19
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Real-time data processing and application performance
Multithreading:
Multiprocessing
Faster for light process
Shared memory
One thread shares the data, the code
Threads take less time to terminate
Communication between threads takes less time than between processes
(This is how the thread works in Python)
GIL
(Global Interpreter Lock), Globale Interpreter-Sperre
Advantage
Disadvantage
Notes: To speed up my application, I thought it would be good to use multithreading or multiprocessing.
1: The first logical option was to use multithreading.
only one thread can execute the Python code at runtime.

## Slide 20
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Real-time data processing and application performance
Multithreading
Multiprocessing:
There is no GIL (Global Interpreter Lock).
When a process is blocked, the remaining processes can continue execution.
A process can run completely independently like a separate program
Processes are completely independent and do not share memory
Processes require more time for creation
Processes require more time for termination
Communication between processes requires more time (QUEUE)
Advantage
Disadvantage
Notes: The second possibility was to use multiprocessing.
One process writes data to the QUEUE, which takes time, and the other reads from the QUEUE, which takes more time.
but I found another solution !!!

## Slide 21
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Real-time data processing and application performance
def for_loop(x):
for i in range(0,x):
x += 2
return x
Cdef def for_loop(int x):
cdef int i = 0
for i in range(0,x):
x += 2
return x
Python :
Cython :
https://en.wikipedia.org/wiki/Cython
Notes: Cython is a general-purpose programming language that is largely compatible with Python.
However, its main advantage is the translation into the target language C, which allows both high performance compared to the standard Python interpreter and direct interaction with external code written in C, C++ or Fortran.

## Slide 22
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Real-time data processing and application performance
Standard deviation of 1e6 elements of the list
Zeit (ms)
https://notes-on-cython.readthedocs.io/en/latest/std_dev.html
https://en.wikipedia.org/wiki/Cython
Cython performance:
Notes: The diagram shows us that the "standard deviation" of a list of one million items is up to 100 times faster in Cython than in Python.
In my application, however, the difference was only 10-20 times faster because my data size was smaller.

## Slide 23
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Server connection
Google Protocol Buffer :
The Google protocol makes it possible to develop universal code for several programming languages from one and the same file.
syntax = "proto3";
package protoblog;
message SSL_DetectionRobot {
  uint32 robot_id = 2;
  float x = 3;
  float y = 4;
  float orientation = 5;
  float pixel_x = 6;
  float pixel_y = 7;
  float height = 8;
  }
Notes: Google protocol provides fast and secure data packets for a server connection.
Google protocol allows to develop a universal code for several programming languages from one and the same file.
This means that by creating a Google protocol, the data is packaged in the format (encoded) and when another language, e.g. C++, connects to the server, the data can be read and decoded. Therefore, the developer on the other side does not have to worry about decoding.

## Slide 24
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Server connection
Server:
The User Datagram Protocol (UDP) is a minimal, connection network protocol that belongs to the transport layer of the Internet protocol family.
UDP enables applications to send datagrams in IP-based computer networks.
Notes: UDP belongs to the Internet protocol family.
 !!! ( Second line )
The advantage of using UDP is that multiple users can receive the same data simultaneously.

## Slide 25
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
Graphical user interface
User interface :
Notes: For the graphical user interface, I used PyQt, a pioneer library for graphical user interface applications using Python.

## Slide 26
Master Ingenieurwissenschaften, Master Angewandte Forschung und Entwicklung Sommer Semester 2022
END
Thank you for your attention